## Slide 1
AST — Audio Spectrogram Transformer
Audio modality encoder · 16:9 widescreen
INPUT · 5 s audio clip @ 16 kHz mono
AST feature extractor (Hugging Face)
Log-mel spectrogram, 128-bin
(T × 128), T ≈ 500
Patch embedding
16 × 16 patches, stride (10, 10)
(N_patches, 768)
Prepend [CLS] token + position embeddings
(1 + N_patches, 768)
Transformer Encoder · × 12 layers
→ see right-side per-layer detail
Extract [CLS] token only
(768,)
AUDIO EMBEDDING · 768-dim → to fusion
Linear ( 768 → 5 ) → audio logits (per-modality CE loss)
Transformer Encoder · per-layer detail
(pre-LN order, repeated × 12)
Multi-Head Self-Attention · 12 heads
+ residual → LayerNorm
FFN ( 768 → 3072 → 768 ) · GELU
+ residual → LayerNorm
(stack of 12 identical layers)
MODEL CARD
Checkpoint:
MIT/ast-finetuned-audioset-10-10-0.4593
Parameters:
≈ 87 M
Pre-training:
AudioSet (2 M clips, 527 classes)
Fine-tune:
5 frozen + 5 fine-tune epochs per subject
Optimiser:
Adam · batch size 8

## Slide 2
ViT — Facial-Emotion Vision Transformer
Vision modality encoder · 16:9 widescreen
INPUT · 5 s video, 25 frames @ 5 fps, 224 × 224 × 3
(25, 3, 224, 224)
── per-frame loop ( × 25 frames ) ──
HF image processor · normalise (μ, σ) per channel
Patch embedding · 16 × 16 patches → 196 patches
linear projection → 768-d per patch
(196, 768)
Prepend [CLS] + position embeddings
Transformer Encoder · × 12 layers
→ see right-side per-layer detail
[CLS] per frame
Mean-pool [CLS] tokens across 25 frames
(768,)
VISION EMBEDDING · 768-dim → to fusion
Transformer Encoder · per-layer detail
(pre-LN order, repeated × 12)
Multi-Head Self-Attention · 12 heads
+ residual → LayerNorm
FFN ( 768 → 3072 → 768 ) · GELU
+ residual → LayerNorm
(stack of 12 identical layers)
MODEL CARD
Checkpoint:
dima806/facial_emotions_image_detection
Parameters:
≈ 86 M
Pre-training:
7-class facial expressions, re-head to 5
Fine-tune:
3 frozen + 2 fine-tune epochs per subject
Per-clip:
Bag-of-frames mean over 25 frames

## Slide 3
EEGNet — Depthwise Separable CNN
EEG modality encoder · 16:9 widescreen
INPUT · 5 s EEG, 30 channels @ 100 Hz
(1, 30, 500)
BLOCK 1 · Temporal + Spatial Filtering
(see right-side expansion)
(64, 1, 125)
BLOCK 2 · Pointwise Separable Conv
(see right-side expansion)
(64, 1, 15)
Flatten · 64 × 1 × 15 → 960
(960,)
EEG EMBEDDING · 960-dim → to fusion
Linear ( 960 → 5 ) → EEG logits
BLOCK 1 · Temporal + Spatial Filtering
Conv2D ( 1 → 8, kernel = (1, 300), pad = same )
BatchNorm2D ( 8 ) → ELU
DepthwiseConv2D ( 8 → 64, kernel = (30, 1), groups = 8 )
BatchNorm2D ( 64 ) → ELU
AvgPool2D ( (1, 4) ) → Dropout ( 0.5 )
BLOCK 2 · Pointwise Separable Conv
Conv2D ( 64 → 64, kernel = (1, 16), pad = same )
BatchNorm2D ( 64 ) → ELU
AvgPool2D ( (1, 8) ) → Dropout ( 0.5 )
MODEL CARD
Architecture:
EEGNet · F1=8, D=8, F2=64, kernLength=300
Parameters:
≈ 2.2 M · trained from random init
Training:
350 epochs per subject · Adam, lr=1e-4
Regularisation:
Dropout 0.5 · L2 max-norm hooks

## Slide 4
TrimodalAttentionFusion — Self-Attention over Modality Tokens
Trimodal fusion module · 2.28 M trainable parameters
x_audio from AST
(768,)
x_vision from ViT
(768,)
x_eeg from EEGNet
(960,)
Linear ( 768 → 256 )
Linear ( 768 → 256 )
Linear ( 960 → 256 )
Stage 1
Projection
+ modality_embed[0]
LayerNorm
+ modality_embed[1]
LayerNorm
+ modality_embed[2]
LayerNorm
Stage 2
Modality
embedding
Stack into sequence · tokens = [audio_tok, vision_tok, eeg_tok] · shape (B, 3, 256)
Softhard Modality Dropout · (training only)
with p = 1/3 · pick m ∈ {audio, vision, eeg} · zero its token
Stage 2.5
robustness
Stage 3 · Transformer Encoder · × 2 layers (pre-LN)
LayerNorm →
Multi-Head SA
8 heads, d = 32
+ residual
LayerNorm →
FFN ( 256 → 1024 → 256 )
GELU
+ residual
Stage 4 · Extract per-modality embeddings + mean-pool fused embedding (B, 256)
FUSED EMBEDDING · 256-dim
Stage 5 · MLP head Linear(256 → 256) → GELU → Dropout(0.1) → Linear(256 → 5) → logits (B, 5)